## Slide 1
QUILL
CO2 Capture from Commercial Flue Gas Process Streams
25th March 2024
Michael Sweeney
Primary Supervisor: Dr. Leila Moura
Co-supervisor: Prof. John Holbrey
Start Date: Oct 23

## Slide 2
Background of the project
1) Regulation (EU) 2021/1119 2) Schlissel D (2018) Holy Grail of carbon capture continues to elude coal industry. Technical report
QUILL
Carbon dioxide (CO2) emissions play a pivotal role in climate change, EU have signed on to stop global temperatures rising above 1.50C greater than pre-industrial temperature.1
Aim to reduce emission by 2030 by 55% from level of 1990
Carbon Neutral by 2050
CO2 capture needed across sectors, recycling, H2 production
Technical report from 2018 says there are serious problems with implementation and operation of CO2 capture systems2
Notes: The four CCS initiatives reviewed here can all be categorized as experimental, and none of the experiments have gone well. Two in essence have been abandoned (Edwardsport and Kemper) and two (Boundary Dam and Petra Nova) are only economically viable by selling the captured CO2 for use in EOR which, in turn adds more CO2 to the atmosphere.
Meanwhile, the utility has had to pay millions of dollars for temporary units that boost the capacity of the system’s thermal reclaimer, the unit that purifies the amine solution used to strip CO2 and sulfur dioxide from the plant’s flue gases. The amine solution has been degrading faster than anticipated, overwhelming the plant’s installed reclaimer and forcing the utility to bring in mobile units.9 The fix has worked, but according to a report prepared for SaskPower, it is “not economically sustainable.”10
So far at a reduction of 26% of 1990 level

## Slide 3: Other CO2 capture methods
X. Wang et al, Front Energy Res, 2020, 8, 560849.
QUILL
Notes: Different routes of CO2 uptake that have been explored. Each has their respect drawbacks.
Cryogenic is very energy intensive
Biological has time constraints forests don’t grow overnight
Membranes degrade quickly and have high maintenance costs
Solids adsorbents have drawback from cleaning and high regeneration cost.
Physisorbants have a lower uptake that chemisorbent materials and rely on pressure Low henry’s constant higher solubilty
Chemisrobents somethings require high temperature

## Slide 4
Goals of the project
G. L. P. Aydos et al, ChemSusChem 2023,16, e2023009
QUILL
Fast kinetics
Reversibility
Low reaction heat
Chemical stability
Thermal stability
Water tolerant
Low volatility
Low viscosity
Chemical
Physical
Ideal
Liquid
Sorbent
Investigate the chemisorption properties in ionic liquids for CO2 capture
Further understand the effects of water on CO2 capture by ILs
Build a database for CO2 capture in ionic liquids (Poster)
Notes: Amine

## Slide 5
Drawbacks;
Very viscous diluted in water to 30 %wt. Water high heat capacity energy intensive to heat to desorption temperatures
Degrade into corrosive by-products
Introduction
Copied2
What is flue gas?
Post-combustion exhaust, primarily N2, 3-15% CO2, O2 & water vapour with other trace impurities (CH4/NOx/SOx)1
1) X. Wang et al, Front Energy Res, 2020, 8, 560849.| 2) B. Dutcher et al, ACS Appl Mater Interfaces, 2015, 7, 2137–2148. |3) NPL REPORT (RES) 1613 |4) Akram eta al, Int. J. Greenhouse Gas Control 95 (2020) 102
QUILL
Current industrial standard?
The current industrial standard for CO2 capture are amine scrubbers, most commonly monoethanolamide (MEA) and other amine blends commonly methyl diethanolamine (MDEA) & piperazine (PZ)
Nitramide
Nitrosamines
Notes: Amine

## Slide 6: Practical work
QUILL
Currently look at these superbasic ILs1 for their chemisorption properties with CO2
Will test the pure CO2 uptake and then CO2/N2 mixture with different levels of water content.
1) Angel et al, J Electrochem Soc, 2022, 169, 086502.

## Slide 7: Practical work
QUILL
1H NMR (DMSO-d6), 400MHz
13C NMR (DMSO-d6), 400MHz
HA
cA
B
C
D
E
F
G
H
I
J
K
L
C,E
HA
L
J,K
I
F,G
B
H
D
CA
L
J,K
F
L
I
B
C E
D
H

## Slide 8: Methodology
Young et al, ACS Sustainable Chem. Eng. 2023, 11, 17787−17796
QUILL
CO2 uptake will be determined by GC-HS method devised by Young et al
Chart: CO2 Calibration Curve @ 35 0C
| 81 | 538 | 977 | 1638 | 2187
 | 5259.3467 | 32779.405 | 54527.5867 | 80527.3833 | 110247.7133

## Slide 9: Quantifying CO2 uptake
QUILL
Chart: Time (hrs)
| 0 | 2 | 21 | 88 | 96 | 116
Pressure Drop | 3000 | 2277.651 | 1564.4875 | 1577.7716 | 1592.0949 | 1598.9775
Chart: Pressure (mbar)
| 3970 | 3505 | 3023 | 2470 | 1975
Initial Pressures | 0.81003 | 0.80556 | 0.73192 | 0.6779 | 0.6128
Final Pressures | 0.81003 | 0.80556 | 0.73192 | 0.6779 | 0.6128
Pressure Range
Equilibrium time @35 0C
ACS Sustainable Chem. Eng. 2017, 5, 8192−8198
Readable Range
Notes: Red lines are the pressure range in which the calibration curve is an optimal accuracy.

## Slide 10: Database
QUILL
Example;
Wang et al, Angewandte Chemie International Edition, 2010, 49, 5978–5981
Cation | Anion | Mw (g/mol) | Water Content (wt%) | Pressure (mbar) | Temp. (K) | CO2 mol/mol IL | CO2 mol/kg IL | CO2 g/kg IL | Mole Fraction | Vis. Pre CO2 (mPa.s) | Vis. Post CO2 (mPa.s) | Desorb. Temp. (K)
[(P2-Et)H] | [PhO] | 433.5 | <0.1 | 1000 | 296.2 | 0.45 | 1.04 | 45.69 | 0.31 | - | - | 353
[MTBDH] | [PhO] | 247.3 | <0.1 | 1000 | 296.2 | 0.49 | 1.98 | 87.20 | 0.32 | - | - | 353
[MTBDH] | [Im] | 221.22 | <0.1 | 1000 | 296.2 | 1.03 | 4.66 | 204.91 | 0.51 | - | - | 353
[MTBDH] | [TFE] | 253.27 | <0.1 | 1000 | 296.2 | 1.13 | 4.46 | 196.40 | 0.53 | - | - | 353
Filtering papers for just CO2 chemisorption ILs, excluding:
Membranes
Polymerised ILs
Grafted / encapsuled ILs
Porous liquids
Amines & amine blends.
Capture all the physical parameters reported,
Temperature
Pressure
Viscosity pre-CO2 & post CO2
Density
Water content
Desorption energy/absorption energy.
Complimentary structural database
Molecular weights
pKa
Abbreviations
# appearances
Notes: Superbasic relies on the pKa of the anion for absorption and the

## Slide 11: Database
QUILL
1) Wang et al, Angew. Chem. Int. Ed. 2010, 49, 5978-5981 2) Latini et al, Journal of CO2 Utilization 2022, 55, 101815
Initial insights from the database include the important of the presence of water, small amounts can increase rate of absorption but can have a negative effect on capacity.
The primary reaction is a carbamate formed with the anion or when water is present there are bicarbonate species present.
Copied2
Copied1
Notes: Superbasic relies on the pKa of the anion for absorption and the

## Slide 12: Future Work
QUILL
Journal of Molecular Structure 1299 (2024) 137133, ACS Sustainable Chem. Eng. 2017, 5, 8192−8198
Potential Cations | Potential Anions
1,8-Diazabicyclo[5.4.0]undec-7-ene (DBU)
Phthalimide (Phth)
Diformylamide (DFA)
1,5-Diazabicyclo[4,3,0]non-5-ene (DBN)
Continue with CO2 uptake testing varying;
-Temperature -Water content
-Test CO2/N2 mixtures
Continue with the adding papers to the database
Investigate new superbasic ILs
Notes: Superbasic relies on the pKa of the anion for absorption and the

## Slide 13
Acknowledgements
QUILL
With thanks to:
Dr. Leila Moura
Prof. John Holbrey
Chevron
Mark Young
Sam McCalmont
Beth Murray
Dr. Yoan Delavoux
QUILL
QUESTIONS?
Funded by CAST Award in Partnership with Chevron & Department of Economy NI