## Slide 1: The formulation of BAL30072 into dosage forms for inhalation
iABC WP2A: Formulation
Consortium meeting June 2016
M Hoppentocht, J Spronk, D Gjaltema and HW Frijlink
Department of Pharmaceutical Technology and Biopharmacy
University of Groningen

## Slide 2: Aims of the project
To develop suitable methods for in vitro evaluation of the newly developed BAL30072 formulations.
  A beta-lactam lab (room 3213.122)
  HPLC method (for analysis)
  Implement equipment (like laser diffractometer)
DPI containing 25 mg and 50 mg BAL30072
Nebulisation solution containing 10 mg/mL and 20 mg/mL of BAL30072
  10, 20, 30, 40 and 100 mg/mL

## Slide 3
Particle processing
  Desired range for inhalation 1-5 microns
  Alpine 50 AS spiral jet mill
Selection of used methods
Multiple characterisation techniques
  DVS, DSC, TGA, SEM
Solutions for nebulisation
  500 mg BAL30072 vials for injection
  Dissolved in 5 mL demineralised water
Notes: The methods used…......

## Slide 4
Laser diffraction analysis with a Sympatec HELOS BF
  RODOS disperser
  INHALER 2000
Selection of used methods
High performance liquid chromatography
  Fast method for inhaler retention
  Basilea method implemented for stability
Inhaler retention
  Gravimetrically
  HPLC
  Effect of lactose sweeper crystals
Notes: The methods used…......

## Slide 5
DPIs
  Twincer®
  Cyclops
Pari Velox
Pari LC Sprint + Turboboy
Pari eFlow
Inhalers (DPIs and nebulisers)
Nebulisers

## Slide 6: Effect of the dose on the dispersion efficiency
Chart: Particle size (µm)
| 0 | 0.9 | 1.1000000000000001 | 1.3 | 1.5 | 1.8 | 2.2000000000000002 | 2.6 | 3.1 | 3.7 | 4.3 | 5 | 6 | 7.5 | 9 | 10.5 | 12.5 | 15 | 18 | 21 | 25 | 30 | 36 | 43 | 51 | 61 | 73 | 87 | 103 | 123 | 147
25 mg | 0 | 8.92 | 14.02 | 19.59 | 25.39 | 34.07 | 45.11 | 54.93 | 65.11 | 74.23 | 80.29 | 84.82 | 89 | 93.19 | 96.04 | 97.75 | 98.95 | 99.64 | 99.94 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100
30 mg | 0 | 8.26 | 12.99 | 18.15 | 23.52 | 31.54 | 41.71 | 50.73 | 60.01 | 68.22 | 73.59 | 77.52 | 81.12 | 84.79 | 87.45 | 89.15 | 90.49 | 91.5 | 92.38 | 93.2 | 94.3 | 95.6 | 96.93 | 98.12 | 99.04 | 99.71 | 100 | 100 | 100 | 100 | 100
40 mg | 0 | 4.42 | 7.75 | 11.73 | 16.13 | 22.95 | 31.88 | 40 | 48.45 | 55.96 | 60.84 | 64.39 | 67.7 | 71.39 | 74.36 | 76.4 | 78.07 | 79.38 | 80.51 | 81.56 | 82.99 | 84.8 | 86.94 | 89.29 | 91.82 | 94.72 | 97.57 | 99.47 | 100 | 100 | 100
50 mg | 0 | 2.77 | 5.33 | 8.55 | 12.19 | 17.94 | 25.56 | 32.52 | 39.76 | 46.11 | 50.11 | 52.87 | 55.32 | 58.02 | 60.35 | 62.03 | 63.47 | 64.69 | 65.86 | 67.02 | 68.69 | 70.99 | 74 | 77.75 | 82.11 | 87.26 | 92.46 | 96.63 | 98.92 | 99.77 | 100
RODOS 3 bar | 25.99 | 36.38 | 45.73 | 54.02 | 64.78 | 76.39 | 84.97 | 92.29 | 97.29 | 99.38 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100
Effect of the dose on the dispersion efficiency of micronised BAL30072 with 2 mg of lactose sweeper crystals (150-200 µm) at 4 kPa pressure drop compared with RODOS 3 bar.
 | X50 | Fpf < 5 µm | Retention (%)
25 mg | 2.39 | 84.82 | 12.21
30 mg | 2.57 | 77.52 | 14.45
40 mg | 3.22 | 64.39 | 14.4
50 mg | 5.36 | 52.87 | 12.49

## Slide 7: Effect of the pressure drop on the dispersion efficiency
Chart: Particle size (µm)
| 0 | 0.9 | 1.1000000000000001 | 1.3 | 1.5 | 1.8 | 2.2000000000000002 | 2.6 | 3.1 | 3.7 | 4.3 | 5 | 6 | 7.5 | 9 | 10.5 | 12.5 | 15 | 18 | 21 | 25 | 30 | 36
2 kPa | 0 | 2.35 | 5.26 | 9.14 | 13.69 | 21.1 | 31.3 | 41.07 | 51.87 | 62.3 | 69.94 | 76.28 | 82.75 | 89.65 | 94.33 | 97.09 | 98.93 | 99.79 | 100 | 100 | 100 | 100 | 100
4 kPa | 0 | 8.92 | 14.02 | 19.59 | 25.39 | 34.07 | 45.11 | 54.93 | 65.11 | 74.23 | 80.29 | 84.82 | 89 | 93.19 | 96.04 | 97.75 | 98.95 | 99.64 | 99.94 | 100 | 100 | 100 | 100
6 kPa | 0 | 9.45 | 14.97 | 21.04 | 27.37 | 36.85 | 48.84 | 59.38 | 70.07 | 79.28 | 84.98 | 88.82 | 92 | 95.05 | 97.25 | 98.51 | 99.21 | 99.46 | 99.49 | 99.54 | 99.68 | 99.88 | 100
RODOS 3 bar | 25.99 | 36.38 | 45.73 | 54.02 | 64.78 | 76.39 | 84.97 | 92.29 | 97.29 | 99.38 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100
Effect of the pressure drop on the dispersion efficiency of 25 mg of micronised BAL30072 with 2 mg of lactose sweeper crystals (150-200 µm) compared with RODOS 3 bar.
 | X50 | Fpf < 5 µm | Retention (%)
2 kPa | 3.01 | 76.28 | 24.41
4 kPa | 2.39 | 84.82 | 12.21
6 kPa | 2.24 | 88.82 | 6.96

## Slide 8: Effect of the pressure drop on the dispersion efficiency
Chart: Particle size (µm)
| 0 | 0.9 | 1.1000000000000001 | 1.3 | 1.5 | 1.8 | 2.2000000000000002 | 2.6 | 3.1 | 3.7 | 4.3 | 5 | 6 | 7.5 | 9 | 10.5 | 12.5 | 15 | 18 | 21 | 25 | 30 | 36 | 43 | 51 | 61 | 73 | 87 | 103
2 kPa | 0.1 | 4.49 | 7.52 | 11.04 | 14.89 | 20.89 | 28.89 | 36.41 | 44.72 | 52.88 | 59.07 | 64.47 | 70.18 | 76.34 | 80.48 | 83 | 84.87 | 85.99 | 86.59 | 86.96 | 87.47 | 88.27 | 89.44 | 90.99 | 92.86 | 95.16 | 97.52 | 99.31 | 100
4 kPa | 0.1 | 4.42 | 7.75 | 11.73 | 16.13 | 22.95 | 31.88 | 40 | 48.45 | 55.96 | 60.84 | 64.39 | 67.7 | 71.39 | 74.36 | 76.4 | 78.07 | 79.38 | 80.51 | 81.56 | 82.99 | 84.8 | 86.94 | 89.29 | 91.82 | 94.72 | 97.57 | 99.47 | 100
6 kPa | 0.1 | 9.88 | 14.69 | 19.56 | 24.38 | 31.28 | 39.7 | 46.91 | 54.15 | 60.44 | 64.52 | 67.52 | 70.32 | 73.24 | 75.42 | 76.95 | 78.38 | 79.7 | 81.19 | 82.62 | 84.51 | 86.4 | 88.73 | 90.64 | 92.52 | 94.77 | 97.24 | 99.23 | 100
3 bar RODOS | 0.1 | 25.99 | 36.38 | 45.73 | 54.02 | 64.78 | 76.39 | 84.97 | 92.29 | 97.29 | 99.38 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100
Effect of the pressure drop on the dispersion efficiency of 40 mg of micronised BAL30072 with 2 mg of lactose sweeper crystals (150-200 µm) compared with RODOS 3 bar.
 | X50 | Fpf < 5 µm | Retention (%)
2 kPa | 3.49 | 60.18 | 25.98
4 kPa | 3.22 | 64.39 | 14.4
6 kPa | 2.81 | 67.52 | 14.97

## Slide 9
Micronisation seems a suitable method to produce inhalable powders of BAL30072.
Administration with the Twincer® seems feasible.
The dispersion efficiency worsens with increasing the dose, whereas the inhaler retention is very constant at different doses and only increases at 2 kPa pressure drop.
Conclusions on DPI development
On going work on DPI development
Force control agents
Spray drying
Other inhalers

## Slide 10
Fine particle fractions at different flow rates for the Pari Velox, Pari LC Sprint and Pari eFlow nebulisers. The Fine particle fraction is the fraction of the droplets smaller than 5.0 µm.
Nebuliser performances with 20 mg/mL BAL30072 (FPF < 5 μm)
Chart: 
| Pari LC Sprint 20mg/ml BAL30072
12 L/min | 0.6732
20 L/min | 0.647
30 L/min | 0.6489
40 L/min | 0.7358
60 L/min | 0.7625
Chart: 
| Pari eFlow 20 mg/ml BAL30072
12 L/min | 0.8124
20 L/min | 0.7668
30 L/min | 0.7542
40 L/min | 0.7361
60 L/min | 0.5128
Chart: 
| Pari Velox 20mg/ml BAL30072
12 L/min | 0.7659
20 L/min | 0.7661
30 L/min | 0.7405
40 L/min | 0.7301
60 L/min | 0.7557

## Slide 11
Droplet size distributions of different BAL30072 concentrations at a flow rate of 30 L/min from the Velox.
Velox performance with different concentrations
Chart: 
| 10mg/ml | 20mg/ml | 30mg/ml | 40mg/ml | 100mg/ml
< 1.1 µm | 0.0399 | 0.0377 | 0.0481 | 0.0274 | 0.0565
1.1-3.1 µm | 0.3677 | 0.4049 | 0.4007 | 0.4353 | 0.4886
3.1-5.0 µm | 0.3008 | 0.2979 | 0.3086 | 0.3053 | 0.2728

## Slide 12
Droplet size distributions of different BAL30072 concentrations at a flow rate of 30 L/min from the eFlow.
eFlow performance with different concentrations
Chart: 
| 10mg/ml | 20mg/ml | 40mg/ml | 100mg/ml
< 1.1 µm | 0.0314 | 0.007 | 0.0195 | 0.0211
1.1-3.1 µm | 0.3451 | 0.3804 | 0.4266 | 0.433
3.1-5.0 µm | 0.3422 | 0.3668 | 0.3474 | 0.354

## Slide 13
Droplet size distributions of different BAL30072 concentrations at a flow rate of 30 L/min from the LC Sprint.
LC Sprint performance with different concentrations
Chart: 
| 10mg/ml | 20mg/ml | 40mg/ml | 100mg/ml
< 1.1 µm | 0.1346 | 0.1344 | 0.1502 | 0.1777
1.1-3.1 µm | 0.2903 | 0.362 | 0.3419 | 0.3991
3.1-5.0 µm | 0.224 | 0.2226 | 0.2183 | 0.2014

## Slide 14
Average retention values of all measurements for each nebuliser with 10, 20 and 100 mg/mL BAL30072 in 5 mL demineralised water.
Nebuliser retention
Chart: 10 mg/mL 20 mg/mL 100 mg/mL
| 10 mg/mL | 20 mg/mL | 100 mg/mL
Pari LC Sprint | 0.30438 | 0.3008 | 0.209
Pari eFlow | 0.34837 | 0.3575 | 0.264
Pari Velox | 0.35675 | 0.3988 | 0.32725

## Slide 15
Nebulisation time
Chart: Concentration of BAL30072 (mg/mL)
| 10 mg/mL | 20 mg/mL | 100 mg/mL
LC Sprint | 5.5 | 5.75 | 6.25
eFlow | 5 | 5 | 6
Velox | 7.25 | 4.5 | 7

## Slide 16
Nebulisation seems a suitable method to administer BAL30072 to the respiratory tract
100 mg/mL BAL30072 nebulisation solution performs best
The eFlow performs best when the FPF, retention and nebulisation times are all considered
However, the performance of the Velox is not much worse and this device is more patient friendly
Conclusions on nebulisation solution development
Ongoing work on nebulisation solution development
Stability of BAL30072 in solution and during nebulisation
Characterisation of BAL30072 solution for nebulisation

## Slide 17
University of Groningen
  Juliëtte Spronk
  Doetie Gjaltema
  Paul Hagedoorn
  Erik Frijlink
Basilea Pharmaceutica
  Stefanie Sämann
  Sofyen Riahi
  Salim Jarri
All other members of WP2
Acknowledgements

## Slide 18: Thank you for your attention
Any Questions?

## Slide 19
Batch | Internal code | X10 (µm) | St.dev. | X50 (µm) | St.dev. | X90 (µm) | St.dev. | FPF < 5 µm (%)
44A | micro151127 | 0.65 | 0.01 | 1.4 | 0.04 | 2.94 | 0.05 | 100
46A | micro160218 | 0.79 | 0.00 | 1.88 | 0.01 | 3.55 | 0.01 | 99.26
47A | micro160219 | 0.74 | 0.00 | 1.74 | 0.00 | 3.36 | 0.01 | 99.68
47A | micro160223 | 0.67 | 0.00 | 1.48 | 0.01 | 2.98 | 0.01 | 100
46A | micro160304 | 0.70 | 0.00 | 1.62 | 0.01 | 3.39 | 0.00 | 96.55
44A | micro160314 | 0.77 | 0.00 | 1.89 | 0.00 | 3.75 | 0.01 | 96.81
46A | micro160317 | 0.82 | 0.02 | 1.93 | 0.03 | 3.58 | 0.02 | 99.22
44A | micro160323 | 0.62 | 0.00 | 1.19 | 0.01 | 2.53 | 0.01 | 100
44A | micro160404 | 0.62 | 0.00 | 1.20 | 0.01 | 2.55 | 0.01 | 100
46A | micro160405 | 0.66 | 0.01 | 1.46 | 0.03 | 3.16 | 0.07 | 97.42
47A | micro160407 | 0.66 | 0.01 | 1.47 | 0.01 | 3.19 | 0.03 | 98.72
46A+2%LL | micro160408 | 0.63 | 0.00 | 1.23 | 0.00 | 2.57 | 0.00 | 100
44A+2%LL | micro160421 | 0.63 | 0.00 | 1.22 | 0.01 | 2.55 | 0.02 | 100
47A+2%LL | micro160429 | 0.62 | 0.00 | 1.17 | 0.00 | 2.45 | 0.01 | 100
47A+2%MgSt | micro160503 | 0.61 | 0.00 | 1.09 | 0.00 | 2.24 | 0.00 | 100
PSDs of micronised BAL30072 batches determined by laser diffraction analysis using a HELOS BF laser diffractometer and a RODOS dry powder disperser operated at 3 bar.

## Slide 20
Batch | Internal code | Temp. during milling (C) | RH during milling (%) | Water content before (%) | Water content after (%) | Milling duration (min.) | Yield (%)
44A | micro151127 | 17 | 44 | 7.7 | 12.5 | 90 (2.8 g) | 50
46A | micro160218 | 17 | 33 | 6.3 | 7.0 | 30 (2.8 g) | 50
47A | micro160219 | 16 | 36 | 4.7 | 8.8 | 30 (2.8 g) | 44
47A | micro160223 | 16 | 36 | 4.3 | 7.5/9.8 | 15 (2.7 g) | 47
46A | micro160304 | 16 | 35 | 6.3 | 8.1 | 37 (2.8 g) | 49
44A | micro160314 | 17 | 35 | 7.7 | 7.2 | 45 (3.0 g) | 59
46A | micro160317 | 16 | 35 | 6.3 | 8.7 | 37 (2.8 g) | 53
44A | micro160323 | 17 | 45 | 7.7 | 8.5 | 180 (3.8 g) | 53
44A | micro160404 | 19-23 | 47-52 | 7.7 | 10.7 | 62 (2.8 g) | 65
46A | micro160405 | 19-21 | 47-52 | 6.4 | 10.9 | 35 (2.3 g) | 58
47A | micro160407 | 18-19 | 37-40 | 4.1 | 9.6 | 27 (2.6 g) | 35
46A+2%LL | micro160408 | 18-19 | 41-42 | 6.4 | 9.5 | 16 (1.5g) | 28
44A+2%LL | micro160421 | 19 | 33 | 7.7 | 8.4 | 19 (1.9g) | 34
47A+2%LL | micro160429 | 16-17 | 42 | 4.1 | 10.3 | 25 (3.5g) | 63
47A+2%MgSt | micro160503 | 18-20 | 40-45 | 4.1 | 9.8 | 31 (3.8g) | 64
47A+2%MgSt* | micro160520 | 19 | 55 |  |  | 18 (1.7g) | 48
47A* | micro160523 | 19 | 60 |  |  | 15 (1.3g) | 38
46A+2%LL | micro160524 |  |  |  |  |  |