## Slide 1: WP6: Novel endpoints
Sputum microbiology
Novel endpoints

## Slide 2: WP6: Sputum microbiology
Screening
  Qualitative microbiology: presence of relevant organisms
  COMBACTE / LAB-Net: quality assurance & training
Clinical studies
  Quantitative microbiology
  Antimicrobial susceptibility testing
Repository of clinical isolates and clinical samples

## Slide 3: Sputum microbiology
Sputum liquefaction
PA selective media
Central Laboratory Manual
Quality control samples
  n=20 in Antwerp & QUB
Local lab feasibility
  COMBACTE questionnaire

## Slide 4: Sputum microbiology: Phase II TIP study
Quantitative culture
  P. aeruginosa
Detection of other potential pathogens
  Haemophilus influenzae, Streptococcus pneumoniae, Moraxella catarrhalis, Staphylococcus aureus
Antimicrobial susceptibility testing
  CLSI broth microdilution/agar dilution
  PA: tobramycin, ciprofloxacin, meropenem, ceftazidime
  Other pathogens: tobramycin
Repository of isolates

## Slide 5: WP6: Integrated development programme for novel endpoints
Exploratory endpoint | Regulatory endpoint | Clinical Trials | WP
Lung Clearance Index (LCI) | FEV1 | TIP Phase II dose finding study: BE BAL30072 Phase IB PK/Safety studies: CF & BE TIP Phase III efficacy /safety studies: BE (in EU) | 4B 3 & 4A 4B
Computed tomography (CT) scanning | FEV1 | TIP Phase II dose finding study: BE TIP Phase III efficacy /safety studies: BE | 4B 4B
Microbiome analysis Resistome analysis | Bacterial load (cfu/g sputum) Resistance development (MIC) | TIP Phase II dose finding study: BE BAL30072 Phase IB Pk/Safety studies: CF & BE TIP Phase III efficacy /safety studies: BE | 4B 3 & 4A 4B

## Slide 6: LCI
25 LCI machines purchased
5 distributed to partner sites
Decision on further 20 sites pending ICON feasibility assessment
Post decision, time required for
  delivery & installation
  training & certification

## Slide 7: LCI: Training, certification and Over reading
Training and certification programme developed and provided by QUB
1st training to 3 partner sites completed (April 2016)
  Papworth, Dundee and Edinburgh
  Certification ongoing: expected June/ July 2016
Machine in place at 2 further partner sites
  Barcelona & Milan
Awaiting decision on location of other machines (ICON feasibility) before booking training
Over reading during trials provided by QUB

## Slide 8: Chest CT image analysis
Ongoing: Preparation for Phase II and III studies
  -Develop CT scan procedure protocols
  -Develop website for chest CT standardization and certification (July 2016: test version)
iABC Phase II study
  -Collect most recent chest CT scans to develop and validate a bronchiectasis CT scoring method

## Slide 9: Chest CT image analysis
iABC Phase III study
  -Standardize CT scanning procedure by interactive web based training
  -Provide site specific feedback on acquired chest CTs via website
  -Analysis of baseline and after-treatment CTs using the developed BE scoring method
  -(Semi)-automatic analysis of airway – artery ratio’s

## Slide 10: Microbiome analysis
Illumina Miseq
Standardized protocols developed
  DNA extraction
  PCR & NGS
qPCR vs. quantitative culture
  P. aeruginosa

## Slide 11: WP6: Sputum inflammatory biomarkers
Exploratory endpoint | Comparison with: | Clinical Trials | WP
Neutrophil elastase, myeloperoxidase, cytokines (e.g. IL-8, IL-6, TNFα, IFNg, IL-1β) | Conventional culture endpoints Exploratory microbiological, LCI and CT endpoints | TIP Phase II dose finding study: BE BAL30072 Phase IB PK/Safety studies: CF & BE | 4B 3 & 4A